## Slide 1
WCE Reporting Tools
Day 1 · WCGRRT and SSORT · Technical Services — Subsea
Notes: Two days. Day 1 is the tools: what they capture, what stops you posting, and why. Led by Dan, with Brad Waldron on SSORT. Seven teaching hours including the exercise.

## Slide 2
SAVED
The file is on your PC.
Nobody else can see it.
Safe from a browser crash — and from nothing else.
You can save as often as you like.
POSTED
The server accepted the file.
The tool checked the response and got a yes.
It is not on the dashboard yet.
This is the only thing the tool can actually see.
ON THE DASHBOARD
The scanner has read the file.
Runs every ten minutes.
This is when other people see your work.
If it is not here, check the Errors button.
Three words that do not mean the same thing
Notes: Spend real time here. Most of the confusion in the field comes from treating these three as one. The tool can only ever tell you the middle one happened. Ten minutes is normal, not a fault.

## Slide 3: The build you are learning
Frozen for the class week
WCGRRT REV 169
Native surface tests, inline references, print page breaks. Photos can be dragged straight onto a photo box.
SSORT REV 165
Test records on any CBM, sent on to NOV. New: model and serial per unit, required by NOV; the Technical Assistance Request; the Argo Navis plan picker and Link to plan; the Daily Log month PDF; FRM-00-0168 Rev 9 additions on the pre-deployment checklist.
Check the badge before you start.
Top of the screen. If it does not match, you are on a cached copy — close it and reopen from the server.
A revision shipped mid-week changes the screenshots. The class trains on one build and one only.
Notes: Confirm the exact SSORT revision with Dan on the morning of the class and write it on the whiteboard. A cached copy is the single most common reason a trainee sees something different from the screen.

## Slide 4
Opening
Lee Arnold · safety minute, roles and responsibilities, expectations for the week · 08:00–08:30

## Slide 5
Module 1
WCGRRT: rig visit and daily reports · 08:30–10:00

## Slide 6: A daily report, blank to saved
What the trainer walks through
Visit Information first.
Rig / Asset is the one field everything else hangs off. Nothing posts without it.
Report Date is not the entry date.
The Report Date sets the filename and files the report. Each entry carries its own date.
One equipment entry per piece of kit.
Type, notes, photographs, captions. Flag it for End of Trip or Critical if it belongs there.
Captions are part of the evidence.
A photograph with no caption is a picture. With one, it is a record.
Save early, save often.
Saving is free and local. Posting is not — it is visible to everyone the moment it lands.

## Slide 7
Two real mistakes
The Capella week, and what it cost
What happened
These are not hypothetical.
Both happened in September, on a real rig, to an experienced supervisor.
Neither was carelessness. Both were the tool letting something through quietly.
REV 161 onwards guards both — but a guard you click past is not a guard.
Mistake | What it did
Posting before finishing | A report was posted, then worked on and posted again under the same filename. The second post replaced the first. One filename, one file.
Entry dates left behind | A draft resumed across several days kept its original entry dates. The filename said the 19th; every entry inside said the 17th.
Why the second is worse | Filing is recoverable. A wrong date printed against a piece of work is not.
Notes: Demonstrate the replace warning on purpose. Post once, change something, post again, and read out the message that tells you the earlier one was replaced.

## Slide 8
Stale entry dates
Any entry dated differently from the Report Date is outlined orange.
Under it: "dated 2026-09-17 — Report Date is 2026-09-19".
A "Set entry dates to this" button appears, and says how many it will change.
Why it does not fix itself
A report can genuinely span two days.
Rewriting the dates would destroy a true fact to fix a common one.
So the tool marks it and offers the fix. It never takes the decision.
Back-dated post
Posting a report dated other than today asks first.
"The date sets the posted filename, so posting it will replace any report already filed for that date."
Cancel, change the Report Date, post again.
The two guards, and what they will not do
Notes: The point of this slide is judgement, not buttons. The tool marks what it cannot safely decide. A trainee who understands why it does not auto-correct will read the other warnings properly too.

## Slide 9
Module 2
WCGRRT: the surface tests and posting · 10:15–12:00

## Slide 10: Five surface tests, all native now
REV 165 and 166 — the embedded tools are gone
BOP Function Test
ILF rows, pod pressures, regulator checks.
EDS Verification
Your rig's own sequences, step by step, with actual times and remarks.
Acoustic Function Test
Rig-specific. Three rigs have no acoustic system and will say so.
EHBS
Three rig classes. DMAS gets a two-part test.
Surface Drawdown
Derived PASS/FAIL — see the next point.
Until REV 165 these were embedded tools and nothing you typed was saved.
It printed and it looked right. It never reached the report. That is fixed; it is also why this module exists.
Notes: Worth saying plainly: the 8-15 September EDS and function test records exist only in the PDFs Brad printed. The data was never in the file. That is what "native" bought us.

## Slide 11
A derived PASS is not a judgement
The drawdown verdict is arithmetic against a published limit.
It says the numbers are inside the boundary. It does not say the system is fit.
Absent means cannot be judged. It never means fail.
Incomplete is not a fail either — it is incomplete.
Inline references (REV 166)
Two per narrative box, labelled REFA and REFB.
Win+Shift+S, then Ctrl+V straight into the text.
For the thing a reader must see there and then — a clause, a drawing detail.
Everything else belongs in the photographs at the end.
Caption them
Say where it came from: document number, revision, section.
Refer to it in the sentence — "outside the limit at REFA".
"See image above" stops making sense once the report is paginated.
Two things to get right in this module

## Slide 12
Module 3
SSORT: CBM inspection and pre-deployment · 13:00–14:30

## Slide 13
Read before you grade
NOV's five-level scale, and what each one means
The scale
99 tasks carry a grade.
85 of them now show NOV's own criteria for that specific item, on the ⓘ button.
14 show the universal scale only.
NOV publishes no item criteria for those. The gap is left visible rather than invented.
A cleaning task carries no grade.
You clean, you photograph. There is no judgement to record.
 | Condition | Verdict
1 | As new | Acceptable
2 | Light wear, within limits | Acceptable
3 | Wear or damage, still serviceable | Acceptable with findings — monitor
4 | Beyond acceptable limits | Not acceptable
5 | Failed or unserviceable | Not acceptable
Notes: Grade 3 is the one people get wrong. It is acceptable with findings — monitor it. It is not a fail, and the dashboard colours it orange to say exactly that.

## Slide 14
What NOV publishes
Across all 44 NOV CBM documents:
3,751 references to grades.
6 references to figures.
Not one line ties a figure to a grade.
There is no NOV photograph of what a Grade 3 looks like.
What the tool shows
51 reference photographs now carry the task they illustrate and the grade they show.
Captioned from Seadrill field experience.
Labelled as such on the screen, every time.
Why that matters
A grade on a reference photograph is one superintendent's read of a picture.
A grade you assign to a component is a record.
Use the first to be consistent. Never confuse it with the second.
Reference photographs — whose judgement is it?

## Slide 15: Pre-deployment, and the cavity record
Two things that will refuse to post
Pre-deployment checklist
The packer attestation is mandatory. Two cavity photographs per cavity — a 7-cavity BOP needs 14.
An incomplete checklist is refused, not warned. The tool names what is missing. New in 165: the Rev 9 additions (ROV panel line-up photos; riser ticks).
Ram Cavity Dimensions
It sits under Calculators and it is not a calculator. It is a dimensional inspection record:
rig, date, supervisor, witness, and PASS/FAIL against TR-WCE-331-038 Rev 3.
Until REV 148 none of it was saved.
Same defect as the surface tests. Everything you type now reaches the report.

## Slide 16: New this month, on SSORT 165
Three things you will meet on the rig
Model and serial: per unit, required by NOV
Read them off the unit for every CBM.
Copy-to-all and Duplicate no longer carry them; Post to OEM asks if they are blank.
Rig down? The Technical Assistance Request
Requests tab. FRM-00-0169 with the DIR-00-0116 deadlines worked out for you.
It says plainly whether the server received it.
Maintenance plan (DL-1) and Link to plan
For Argo Navis plans: every post carries the plan, and Link to plan files the evidence against the task. No plan yet: it says so, and posts go out as normal.

## Slide 17
Module 4
Exercise · 14:45–17:00

## Slide 18
What you produce
One daily report with two equipment entries.
One surface test.
One CBM inspection on Riser Adapter, with its model and serial and a test record attached.
One pre-deployment checklist to the attestation.
Asset: SSCE Equipment. Always.
You post these for real. SSCE Equipment never enters a fleet count, and the class’s posts are deleted afterwards.
Three traps, on purpose
A photograph with no caption.
An entry left on yesterday's date.
A grade recorded with no photograph behind it.
Each one is something the tools have seen in the field.
What to notice
Which traps the tool catches, and how loudly.
Which it lets through, and why that is deliberate.
One report at a time: post it, New Trip, then the next one.
Your own report date. It is the only thing keeping your work apart from everyone else’s.
The exercise, and the traps in it

## Slide 19
Every check the tools make before Post
What stopped you | Tool | Effect | What it means
Rig / Asset not set | Both | REFUSED | A post with no rig cannot be attributed and will not appear against your rig.
Confirm before posting | Both | ASKS | "Once posted it is visible to everyone with dashboard access — only post a finished report."
Report dated other than today | WCGRRT | ASKS | The date sets the filename, so it will replace any report already filed for that date.
Entry dates ≠ Report Date | WCGRRT | MARKS | Outlined orange with the two dates. One button fixes them. Never automatic.
Over 10 MB | Both | WARNS | Accepted anyway. Photos are almost always the cause. Never reduce photo quality to get under it.
Over 40 MB (CBM / PDC) | SSORT | WARNS | CBM and pre-deployment get their own ceiling. Same rule: the evidence is worth more.
Pre-deployment incomplete | SSORT | REFUSED | Names what is missing. The packer attestation and the cavity photographs are mandatory.
Post to OEM over 30 MB | SSORT | REFUSED | Split by equipment section. Do not delete or retake photographs to get under it.
Post to OEM, no equipment | SSORT | REFUSED | "Select the equipment first."
Attachment over 20 MB | SSORT | REFUSED | Refused as you attach it, not at Post. Re-export it smaller or attach the pages that matter.
Attachment over 8 MB | SSORT | WARNS | A PDF or Office file cannot be compressed the way a photograph can.
Attachments over 15 MB in total | SSORT | WARNS | Names the running total against the 40 MB ceiling. Nothing is refused at this size.
Executable or unlisted file type | SSORT | REFUSED | PDF, image, CSV, text or Office only.
The post itself failed | WCGRRT | TELLS YOU | Warns with the HTTP code. The file is still saved locally. Nothing is lost.
The post itself failed | SSORT | SILENT | No warning on Post Report. It can still say "posted". Link to plan and the assistance request do tell you.
Notes: This is the workbook's "why did it stop me" table. Every line was read out of the shipped code for the revisions named on slide 3. If a trainee hits something not on this list, that is worth reporting.

## Slide 20
What appears
WCGRRT
"⚠ Dashboard post failed (HTTP 500) — file still saved locally."
SSORT
No warning at all. You get "Report posted to the shared folder", or a tick and the word saved.
WCGRRT checks the server’s answer and tells you. SSORT does not.
What it means
Your work is not lost. It is in your reports folder or on your PC.
The server did not take the file.
Nothing reached the dashboard, and nobody has seen it.
In SSORT the word "posted" can appear on a failure. Read which thing it says.
What you do
1. Save the file if you have not.
2. Try Post again — most failures are the network.
3. Check the dashboard after ten minutes. That is the proof, not the message.
4. Still missing? Send the saved file to the office and tell someone.
Never assume it went.
When Post fails — what you see, what you do

## Slide 21
The report is the evidence that the BOP was fit to run. Everything else is housekeeping.